- Classification of scrap batch

| EUROPEAN CATEGORY | POLISH CATEGORY | DESCRIPTION OF SCRAP TYPES | DIMENSIONS (metres) | THICKNESS |
| --- | --- | --- | --- | --- |
| E3 | W7 | Post-amortisation and selected old scrap, heavier scrap with permissible dimensions and thickness (specified next to the text). This class can include thick pipes. Car bodies are not acceptable. | 1,5x05x05 | > 6 mm |
| E1 | W2 | Lighter and thinner scrap. Parts of lighter vehicles are acceptable. This class neither includes car bodies nor household appliances. Wires, rods, machine parts, pipe parts with a diameter of up to 100mm are acceptable. | 1,5x05x05 | > 3 mm |
| E4 | W5 | Old scrap, which is at least 10 mm thick, from industrial demolitions, e.g. constructions, machine elements and components of railway demolitions, such as: rails, wheels, axles, chassis rail. Scrap shear, pieces of pipes, wires, wire products, ropes and chips are not permitted. | 1,5x0,5x05 | > 10 mm |
| E2 | W7n | New, post-production scrap from ironwork (except chips). It must not be in a form of badly compressed packets. No tin, copper, lead, metal alloys, machine parts and debris. | 1,5x0,5x05 | > 4 mm |
| E8 | W7n | New and thin, post-production scrap from ironwork (except chips). It must not be in a form of badly compressed packets. No tin, copper, lead, metal alloys, machine parts and debris. | 1,5x0,5x05 | < 4 mm |
| E6 | W10n | New, post-production, light scrap. Pressed into blocks. In a form of packages. It must not contain tin, copper, lead, metal alloys, machine parts and debris. | 1,0x0,5x0,5 |  |
| E5 | W13 | Mixed carbon steel chips, must not contain scrap from automatic machines, free from scale and grinding dust. | < 150mm długości |  |

- Classification of nonbatch scrap.

| POLISH CATEGORY | DESCRIPTION OF SCRAP TYPES | DIMENSIONS (metres) | THICKNESS |
| --- | --- | --- | --- |
| N-10 | Mixed, post-amortisation steel scrap, car bodies without non-metallic elements are allowed. | 3,0x1,5x1,0 | < 4 mm |
| N-2 | Post-amortisation steel scrap, up to 3mm thick, ready for packaging in a form of sheets, open-works, flat bars, pipes, strips, car body parts without chassis and scrap with non-ferrous metal coating. Spatial dimensions of this scrap should not exceed: 3000x1200x1000mm. | 3,0x1,5x1,0 | < 3 mm |
| N-7 | Post-amortisation, steel, nonbatch, large-scale scrap from industrial demolitions, e.g. lightweight constructions, parts of machines and profiles, pipes with a diameter of up to 150mm intended for cutting with blowtorches or scrap shear. Wire scrap, wire products, ropes and chips are not accepted. | Wg uzgodnień z odbirocą | > 5 mm |
| N-5 | Post-amortisation, steel scrap which is difficult to cut with blowtorches or scrap shear, in a form of construction elements, profiles, sheet piling, railway and mining components, etc. | 5,0x1,0x1,0 | > 10 mm |
| N-1N | Post-production, thin, steel scrap suitable for packaging, derived from production facilities (galvanised scrap allowed). It must not contain tin, copper, lead, metal alloys, machine parts and debris. | 3,0x1,0x0,5 | < 3 mm |
| N-6 | Scrap in a form of a standard gauge railway and tram tracks without accessories (bolts and washers). | dł. max 12m |  |
| N-3 | Steel ropes scrap up to 30mm thick, strips, wires in coils or wire bundles of any size, up to 400kg, enabling loading and unloading. |  |  |
| N-4 | Mixed carbon steel chips, free from scale and grinding dust. |  |  |